## Slide 1: Real‑Time 7‑Band Speech Scrambler
FIR Filterbank + Cosine Modulation-Encoder
Suravi Das -100004524 M.Sc. (IT–AI), SRH Hochschule Heidelberg
LinkedIn:https://www.linkedin.com/in/suravi-das-44a8552b7/

## Slide 2: Assignment & Objectives
Explaining the assignment: We build a working speech scrambler encoder and explaining the design
Objectives: (1) Decompose bands, (2) Frequency shift, (3) Constrain to target band, (4) Recombine
Demonstrate correctness: audio evidence + spectrograms
Discussion on key code components: filter design, mixing, mapping
Justify choices: FIR+Kaiser, transition fraction, 7 equal-width bands, real cosine
Notes: Tie to rubric.

## Slide 3: System Overview
Pipeline: Input → Analysis FIRs → Band mapping → Cosine mixers → Synthesis FIRs → Output
Mixer: m[n] = 2 · cos(2πΔf · n / f_s)
Δf = f_target,center − f_source,center; post-mix re-filter removes the image band
Linear-phase FIRs → predictable group delay and clean recombination
Notes: Block diagram narrative + formula.

## Slide 4: Filterbank Design (FIR + Kaiser)
Design: scipy.signal.firwin(pass_zero=False, window=('kaiser', β))
β from stopband attenuation A (dB): Kaiser empirical formulas
Transition width: tw = transition_fraction × (f_hi − f_lo)
Odd numtaps ≥ 101; conservative kaiserord-style length estimate
Trade-off: better stopband ↔ longer delay/CPU
Notes: Why FIR/kaiser.

## Slide 5: 7‑Band Layout (fs = 16 kHz)
Nyquist f_N = 8 kHz; Equal-width bands over [0, f_N]
Per-band width: f_N / 7 ≈ 1142.86 Hz; centers step by ≈ 1142.86 Hz
Centers ≈ [571, 1714, 2857, 4000, 5143, 6286, 7429] Hz
Transition fraction 0.12 narrows passbands to reduce leakage
Notes: State numeric centers.

## Slide 6: Mixing Mathematics
Cosine identity: cos θ = ½(e^{jθ} + e^{−jθ}) → creates ±Δf sidebands
Multiply y_src[n] by m[n] and re-filter with target bandpass
Amplitude factor 2 compensates for single-sideband selection after filtering
Linear-phase FIRs preserve waveform symmetry; frequency location changes
Notes: Short and clear.

## Slide 7: Scrambling Mapping Example
Output order: [7, 5, 3, 1, 2, 4, 6] (input→output)
Δf (Hz): 1→7: +6857, 2→5: +3429, 3→3: 0, 4→1: −3429, 5→2: −3429, 6→4: −2286, 7→6: −1143
Target filter confines shifted band; mirror image rejected
Mapping configurable: intelligibility vs obfuscation
Notes: Matches earlier math.

## Slide 8: Demo (1): Clean Speech
Play: clean.wav (3–5s, mono, 16 kHz)
Show: waveform + linear-frequency spectrogram (n_fft=2048, hop=512)
Observe: intact formants and harmonics
Notes: Fallback to pre-rendered files.

## Slide 9: Demo (2): Scrambled Speech
Play: scrambled.wav (same clip after scrambling)
Show: spectrogram with new band centers; annotate arrows
Perceptual effect: intelligibility reduced, energy preserved
Notes: Level-match audio.

## Slide 10: Code Essentials: Filter Design
β & taps length (conservative):
beta = 0.1102*(A-8.7) (A>50); else β = 0.5842*(A-21)^0.4 + 0.07886*(A-21) (A≥21)
delta_f = tw/(fs/2); N_est ≈ (A-8)/(2.285·2π·delta_f); numtaps = odd ≥ 101
firwin(numtaps, [f1/nyq, f2/nyq], pass_zero=False, window=('kaiser', β))
Notes: Snippets as bullets.

## Slide 11: Code Essentials: Scrambling Loop
Centers: f_src_c = (src_lo+src_hi)/2; f_tgt_c = (tgt_lo+tgt_hi)/2; Δf = f_tgt_c − f_src_c
mixer = 2*np.cos(2πΔf * n / fs); shifted = y_src * mixer
confined = lfilter(tgt_taps, [1], shifted); out += confined
Sum all confined bands → scrambled output
Notes: Map bullets to code lines.

## Slide 12: Results, Limitations & Next Steps
Results: band relocation visible; audible scrambling achieved
Limitations: group delay; edge bands; CPU for long filters
Next: delay compensation; overlap-add; perceptual banding; streaming
Notes: Close with roadmap.

## Slide 13: Appendix A1 — Taps vs Attenuation vs Transition
Longer taps → narrower transitions, better stopband, higher delay/CPU
Balanced default: A≈40 dB; transition_fraction≈0.12
Tune if leakage observed
Notes: Rules of thumb.

## Slide 14: Appendix A2 — Group Delay & Compensation
Each FIR adds (L−1)/2 samples; analysis+synthesis accumulate
Compensate via trimming/padding or shifting playback
Quantify latency for real-time apps
Notes: Practical hints.

## Slide 15: Appendix A3 — Complexity Estimate
Cost ~ O(N_bands · numtaps · Fs) for direct convolution
Use FFT overlap-add for long filters; vectorize
Process audio in streaming blocks
Notes: Back-of-envelope complexity.