## Slide 1: Real‑Time 7‑Band Speech Unscrambler / Decoder
FIR Filterbank + Cosine Modulation
Soumya Banerjee — M.Sc. (IT–AI), SRH Hochschule Heidelberg
GitHub: https://github.com/SOUMYABAN123 | LinkedIn: https://www.linkedin.com/in/soumya-banerjee-5aa65b191/
October 08, 2025

## Slide 2: Assignment & Objectives
Implement and demonstrate a working unscrambler
Steps: (1) Analysis filterbank, (2) Inverse permutation, (3) Cosine shift, (4) Synthesis
Evidence: waveform + spectrogram before/after; audio clips
Discuss core code: inverse mapping, Δf_dec, filters
Justify design: matched FIRs, linear phase, Kaiser window
Notes: Align with rubric.

## Slide 3: Decoder System Overview
Scrambled Input → Analysis FIRs → Inverse Mapping → Mixers → Synthesis FIRs → Output
Mixer: m[n] = 2 · cos(2πΔf_dec · n / f_s)
Δf_dec = f_orig,c − f_scrambled,c; re-filter selects desired sideband
Group delay from FIRs; handle alignment
Notes: High-level view.

## Slide 4: Filterbank Reuse (FIR + Kaiser)
Same β, transition_fraction, and numtaps as encoder for matched response
Odd numtaps ≥ 101 for linear phase and symmetric impulse response
Trade-offs as in encoder: stopband vs delay/CPU
Notes: Matched analysis/synthesis.

## Slide 5: Inverse Permutation
Encoder mapping: [7, 5, 3, 1, 2, 4, 6] (input→output)
Inverse: inv[p[i]] = i → inv = [4, 5, 3, 6, 2, 7, 1] (encoded→original)
Encoded band k goes to original band inv[k] via Δf_dec
Notes: Permutation algebra.

## Slide 6: Mixing Mathematics (Decoding)
For encoded band k: Δf_dec = f_c[inv[k]] − f_c[k]
m[n] = 2 · cos(2πΔf_dec · n / f_s) → ±Δf images
Target bandpass confines to original band and rejects mirror image
Amplitude factor 2 compensates for single-sideband selection
Notes: Keep sign and indices correct.

## Slide 7: Synchronization & Delay
Each FIR adds (L−1)/2 samples; analysis+synthesis accumulate
Trim/pad or shift to align with original for evaluation
Stream in blocks with overlap to avoid edge artifacts
Notes: Practical timing issues.

## Slide 8: Demo Plan
Input: scrambled.wav (3–5s, mono, 16 kHz)
Show: scrambled spectrogram
Decode with inverse mapping; output: decoded.wav
Show: decoded spectrogram; compare with original (if available)
Notes: Concise, reliable demo.

## Slide 9: Code Essentials: Inverse Mapping & Δf
Compute band edges/centers; build inv permutation
Δf_dec per band using centers (Hz)
Mixer generation and application; vectorized where possible
Notes: Map to notebook cells.

## Slide 10: Code Essentials: Filtering & Recombination
confined = lfilter(taps[target], [1], encoded_band * mixer)
Sum confined bands; optional normalization and DC removal
Handle group delay (trim/pad)
Notes: Synthesis details.

## Slide 11: Results & Evaluation
Spectrograms: scrambled vs decoded (bands back to originals)
Subjective intelligibility restored; optional metrics (SNR/LSD)
Notes on any residual artifacts and their cause
Notes: Show it works.

## Slide 12: Design Choices & Limitations
Matched FIRs (Kaiser, ~40 dB stopband) and equal-width bands
Trade-offs: taps vs CPU/delay; transition width vs leakage
Failure modes: wrong mapping, Δf sign, drift/sync issues
Next: adaptive detection, Hilbert SSB, perceptual banding
Notes: Wrap up.

## Slide 13: Appendix A1 — Robustness
Noise: filtering helps but cannot recreate missing info
Clock drift: resampling/sync correction may be required
Quantization: 16‑bit is fine; keep headroom
Notes: Operational.

## Slide 14: Appendix A2 — Complexity & Optimization
O(N_bands · numtaps · Fs) for direct convolution
FFT overlap‑add for long taps; vectorize mixers
Block streaming for real-time
Notes: Performance.

## Slide 15: Appendix A3 — Validation Checklist
Verify inv[p[i]] = i with unit tests
Tone test per band to verify Δf_dec signs
Spectrogram check: centers align with originals
Notes: Checklist.